## Slide 1
Robotic Positioner
PRESENTED BY GROUP 5: Thomas Hu, Jordan Smith, Jason Wong
Add things here if needed

## Slide 2
01
TOPIC HIGHLIGHTS
Overview
Problem Description
Requirements Analysis
System Alternatives
System Design
Q&A

## Slide 3
PROBLEM DESCRIPTION
02

## Slide 4
03
Problem Definition
A device which can be used to rotate equipment for welding, blasting, painting, or finishing that can be mounted to their existing rotator frames.

## Slide 5
Why is this important?
Advancing mechanical machines forward with electronics.
Provides a safer environment for the users.
Improves efficiency.
04

## Slide 6
Problem Statement
“There exists a need for a low cost system that can electrically rotate a load for welding applications to increase efficiency and safety.”
05

## Slide 7
REQUIREMENTS ANALYSIS
06

## Slide 8
Design Requirements
The system must rotate a load 360 around a horizontal axis
Be able to recall and rotate to 4 different angle positions (physical buttons & E-stop)
Must be able to support up to max load of 500 kilograms (kg)
The speed of the rotations must be 1-5 rpm
07
The system shall be built using two “A” frame supports provided by the client
Total cost of the system components must not exceed $10,000 Canadian Dollars
All components used are RoHS compliant

## Slide 9
Requirements Justification
Device enclosure requirement
Operating in an industrial environment
Must be able to support up to max load of 500 kilograms (kg)
The speed of the rotations must be 1-5 rpm
08

## Slide 10
SYSTEM ALTERNATIVES
09

## Slide 11
Motor Alternatives
Induction Motors
Pros
  Inexpensive
  Easy to maintain
Cons
  Speed control is very limited and expensive via variable frequency drive
  High in rush current when heavy loaded
  Requires external positioning sensors
10

## Slide 12
Motor Alternatives
Stepper Motors
Pros
  High torque at lower speeds
  Relatively simple operation
  Possible to operate in closed loop feedback eliminating external sensor
Cons
  Sudden drop off in torque as speeds increase
  Noisy
  Requires external driver
11

## Slide 13
Microcontroller Alternatives
Teensy 3.6
Pros
  Powerful with lots of pins and ports
Cons
  Difficult setup period
  Limited library
12
TI Launchpad MSP432P401R
Pros
  Inexpensive
  Extensive library
  Expandable memory
Cons
  Limited pins

## Slide 14
Choosing A System
Employed a weighted decision matrix based on requirements and safety considerations
13
Requirement | Weight | Arduino Uno | Teensy 3.6 | Ti LaunchPad
Power | 5.00% | 2 | 1 | 3
Cost | 20.00% | 2 | 1 | 3
No. GPIO | 25.00% | 2 | 3 | 1
Reliability/Support | 15.00% | 3 | 2 | 1
Memory Size | 15.00% | 1 | 3 | 2
Compatibility | 20.00% | 3 | 2 | 1
TOTAL | 100.00% | 2.2 | 2.15 | 1.65

## Slide 15
SYSTEM DESIGN
14

## Slide 16
Hardware Design
System-Level Block Design
15

## Slide 17
Software Design
System-Level Block Design
16

## Slide 18
Subsystems
MICROCONTROLLER
A compact integrated circuit designed to operate the motor.
MOTOR
Rotates the gearbox to do something
ENCODER
A motor mounted encoder provides closed loop feedback signals to communicate the speed and position of the motor shaft.
GEARBOX
A mechanical drive to step down the speed of rotation from the motor shaft to the output drive, proportionally increasing the torque.
17

## Slide 19
Servo Motor
Pros
  Encoder allows for a closed loop feedback operation
  Near constant torque within operational speeds
  Integrated encoder for high precision position tracking
Cons
  Expensive
18

## Slide 20
Arduino Uno R3
Pros
  Quickly prototype projects on to it
  Store and analyze data for a motor
  Easy to use
  Compatibility with motor
Cons
  Limited processing power
Microcontroller
19

## Slide 21
Q&A
20