## Slide 1
Robotic Positioner
PRESENTED BY GROUP 5: Thomas Hu, Jordan Smith, Jason Wong

## Slide 2
Agenda
Doepker Industries Ltd
Problem Description
Requirements Analysis
System Alternatives
System Design

## Slide 3
DOEPKER INDUSTRIES LTD

## Slide 4
About Doepker Industries
Provides value in the transportation industry in North America
  Agriculture
  Flat decks
  Oil & gas
  Forestry
  Gravel
  Heavy haul

## Slide 5
PROBLEM DESCRIPTION

## Slide 6
Problem Definition
A device which can be used to rotate equipment for welding, blasting, painting, or finishing that can be mounted to their existing rotator frames.

## Slide 7
Currently uses mechanical equipment
Advancing mechanical machines forward with electronics.
Provides a safer environment for the users.
Improves efficiency.
Why is this important?

## Slide 8
Problem Statement
“There exists a need for a low-cost system that can electrically rotate a load for welding applications to increase efficiency and safety.”

## Slide 9
REQUIREMENTS ANALYSIS

## Slide 10
Design Requirements
rotate a load 360˚ around the horizontal axis
recall and rotate to a preset angular position
support up to max load of 500 kilograms
have a rotation speed between 1-5 rpm
be built using two “A” frame supports
not exceed $10,000 Canadian Dollars to build
use RoHS compliant components
The System Shall:

## Slide 11
SYSTEM ALTERNATIVES

## Slide 12
Motor Alternatives
Induction Motors
Pros
  Inexpensive
  Easy to maintain
Cons
  Speed control is very limited and expensive via variable frequency drive
  High in rush current when heavy loaded
  Requires external positioning sensors

## Slide 13
Motor Alternatives
Stepper Motors
Pros
  High torque at lower speeds
  Relatively simple operation
  Possible to operate in closed loop feedback eliminating external sensor
Cons
  Sudden drop off in torque as speeds increase
  Noisy
  Requires external driver

## Slide 14
Motor Alternatives
Servo Motors
Pros
  Encoder allows for a closed loop feedback operation
  Near constant torque within operational speeds
  Integrated encoder for high precision position tracking
Cons
  Expensive

## Slide 15
Control System Alternatives
FPGA
Pros
  Precise PWM motor control
  Optimal performance
Cons
  Time intensive software development
  Difficult memory management
  Can be expensive
Notes: Pros: powerful, better optimization of the program

## Slide 16
Control System Alternatives
Programmable Logic Controller (PLC)
Pros
  Reliability
  Remote control
  Possible to operate in closed loop feedback eliminating external sensor
Cons
  Expensive
  Not much benefit for this application

## Slide 17
Control System Alternatives
Microcomputer
Pros
  Simple learning curve
  Powerful in terms of processing power
Cons
  Analog to digital conversion
  Less accurate timing control
  SD card will wear out
Notes: Cons: less flexible when it comes to real-time and analog usage (ex. Sensors and chips)
- Reading analog sensors require extra hardware assistance

## Slide 18
Control System Alternatives
Microcontroller
Pros
  Quickly prototype projects
  Robust memory management
  Abundant or expandable pins & ports
  Reasonable learning curve
  Inexpensive
Cons
  Reliability

## Slide 19
Choosing A System
Employed a weighted decision matrix based on requirements and safety considerations:
Requirement | Weight | FPGA | PLC | Microcomputer | Microcontroller
Cost | 20% | 2 | 1 | 3 | 4
Memory Management | 20% | 1 | 2 | 3 | 4
Compatibility | 20% | 4 | 2 | 1 | 3
Reliability | 20% | 4 | 3 | 1 | 2
Development | 20% | 1 | 3 | 2 | 4
TOTAL | 100% | 2.4 | 2.2 | 2 | 3.4

## Slide 20
SYSTEM DESIGN

## Slide 21
Key Components
MICROCONTROLLER
A compact integrated circuit designed to operate the motor.
SERVO MOTOR
A rotary actuator or linear actuator that allows for precise control of angular or linear position, velocity and acceleration.
ENCODER
A motor mounted encoder provides closed loop feedback signals to communicate the speed and position of the motor shaft.
GEARBOX
A mechanical drive to step down the speed of rotation from the motor shaft to the output drive, proportionally increasing the torque.

## Slide 22
Hardware Design
System-Level Block Design

## Slide 23
Software Design
System-Level Block Design

## Slide 24
Q&A