## Slide 1: Robotic positioner
Presented by group 5: Thomas hu, Jordan smith, Jason wong

## Slide 2: Overview
Problem Description
Requirements Analysis
System Design
Detailed Design and Testing
Demonstration
Design Discussion

## Slide 3: Problem description

## Slide 4: Problem Statement
“There exists a need for a low-cost system that can electrically rotate a load for welding applications to increase efficiency and safety.”

## Slide 5: Why is this important?
Currently only uses mechanical rotators.
Advancing mechanical machines forward with electronics.
Provide a safer environment for the users.
Improves efficiency.

## Slide 6: Requirements analysis

## Slide 7: Design constraints/requirements
The System Must:
Retrofit Doepker’s existing support frames.
Use an electric motor.
Not exceed $10,000 Canadian Dollars to build.
Be controlled using physical buttons on a control panel.
The System Shall:
Have a rotation speed between 1-5 rpm.
Recall and rotate to a preset angular position.
Require a safety button to be depressed to operate the system.
Be operated from a control panel separated from the rotating portion of the system
Support up to max load of 500 kilograms.
Rotate a load 360˚ around the horizontal axis.

## Slide 8: System design

## Slide 9: System diagram – hardware systems
MOTOR
E-STOP
POWER
DISTRIBUTION
PANEL
REMOTE CONTROL
230 VAC
230 VAC
230 VAC
CONTROL SIGNAL
CONTROL SIGNAL
12 VDC

## Slide 10: System diagram – software diagram

## Slide 11: Detailed design & testing

## Slide 12: Remote
Button press to trigger events:
  Enable(hardwired to control voltage for button commands)
  Clockwise rotation
  Counter clockwise rotation
  CW and CCW 45 degree advance
  Home(returns to zero)/set home
  Stop/Reset
  Emergency stop

## Slide 13: Motor control
Microcontroller was used to control a 12VDC signal via transistor
Base current limiter used to protect the circuit even in the case of a short circuit

## Slide 14: Motor Control
Frequency controlled operation
Originally used a 10kHz pulse
  Firing circuit too slow
  Caused duty cycle to be nearly 70%
Decided to use a 5kHz pule
  Achieved a duty cycle of 55%

## Slide 15: Motor Positioning
Motor encoder
  4 pulses per revolution(PPR)
  Motor operating at 500rpm to achieve 1rpm on robotic positioner
  Arduino receives pulses at a frequency of 33.3Hz

## Slide 16: Emergency stop
Both the digital signal and hardwired E-Stop button must be logic high
Base current limiter incorporated for short circuit protection
Fly-back diode used to protect the circuit from change in inductive load

## Slide 17: Software - code
Calculates the amount of degrees it needs to rotate.
  Reading for changes for the pins
  Once a pulse is read it adds to the pulse count and increments the position.
Multiple functions to handle each task.
  Wait for rotations to finish
  Rotate function
  Stop rotating function
Everything else for the code was straight forward with the use of TimerOne and encoder library.

## Slide 18: Proof of concept testing
Incremental Subsystem Testing
Tested each subsystem as they were built.
Verified that each subsystem performed as expected.
Verified individual software functions:
  Buttons
  Rotations
  E-stop/stand by states
Complete System Testing
Moved hardware from breadboard to proto-board.
Connected each subsystem as outlined in system diagram.
Tested outline functionalities:
  Each type of rotation
  Button presses
  Speed of rotation
  Correct rotation angles

## Slide 19: Demonstration

## Slide 20: Design discussion
Limitations and future work

## Slide 21: Challenges faced
Hardware/Software interfacing.
Hard design to a proof of concept.
Mechanical Binding
Noise
Avoidable mistakes
Covid-19

## Slide 22: Mechanical binding
A welding seam was contacting a nut on the adapter collar
  Dismantled the reducer and ground down the nut

## Slide 23: noise
Arduino is susceptible to noise
  Electrolytic capacitor added to filter the DC voltage

## Slide 24: Avoidable mistakes
Accidentally contacted two terminals when testing the circuit causing a short circuit
  Replacement parts are on order
https://scifi.stackexchange.com/questions/7511/why-do-consoles-explode-in-star-trek/95241

## Slide 25: Covid-19
Unable to test the fully integrated system with the motor
Unable to test the torque at Doepker Industries

## Slide 26: Current system limitations
Can only change speed of rotation in the code.
Handling load all on one side.

## Slide 27: Future Design work
Design a proper PCB for the controller or use a PLC.
A speed setting for how fast/slow the positioner rotates.
Additional IO to verify events
  External sensor to check if E-Stop triggers
  External sensor on enable

## Slide 28: Thank You! Questions?
Jordan smith
Thomas hu
Jason wong